Changes in the program version 18.0 compared with the 17.0 program version

1. Extra column "Availability" is added to the tables of the program containing the roller shutter components. This column defines the fact of the particular component availability (color scheme of the table column-row based on the value in this column is carried out in the dialog window "Parameters / Other"). Data for this column is taken from the price-list specified for the order (values for this column are entered in the "Price lists" dialog window on the tab "Price lists for components").

2. New currency – Belarusian Ruble (BYN) has been added to the program.

3. All tubular motors “AN-MOTORS”: "NK1/10-16", "NK1/15-16", "NK1/20-16", "NK1/30-16", "NK1/40-12", "NK1/50-12", "NR0/06-28", "NR0/10-16", "NR2/100-12", "NR2/140-8", "NR2/60-12", "NR2/80-12", "NM1-PP/20-16", "NM1-PP/30-16", "NM1-PP/40-12", "NM1-PP/50-12", "NM2-PP/100-12", "NM2-PP/140-8", "NM2-PP/60-12" and "NM2-PP/80-12"  have been deleted from the program.

4. When calculating the roller shutter in the window with tubular motors the filter according to the manufacturer "SOMFY" is not marked.

5. When calculating the roller shutter in the window with tubular motors the additional filter according to the manufacturer "SOMFY" (Simu*, Compact*)” is presented.

6. Parameter value “Producer” has been changed from “SOMFY“ to “SOMFY (Simu*, Compact*)“ for the following tubular motors: "Compact 200/12W", "Compact 300/12", "Compact 400/8", "Simu T820M" and "Simu T825M".

7. When calculating the roller shutter with “Safety edge” system selection of radio control “Radio 8113-IP65“ is allowed.

8. When calculating the roller shutter selection of radio control “Radio 8113 IP65M-sensor” is not allowed (it could be added to the specification manually only).

9. New side cap “SF360m“ has been added to the program.

10. New guide rails “GR60x21/SI“ and “GR60x21/SE“ have been added to the program.

11. New security lock ring “R70/S“ has been added to the program.

12. New reinforcement plate for shutter box “SBS300“ has been introduced to the program (it could be added to Specification manually only).

13. New system of manual override blocking “S-NHK“ has been introduced to the program (it could be added to Specification manually only).

14. When calculating the roller shutter if one of the following shutter boxes “SB45/230”, “SB45/360-MH”, “SB45/360” or “SB45/405” is chosen, two additional stoppers “ST25” will be added to Specification.

15. When calculating the roller shutter with integrated anti-mosquito net if 137mm shutter box is chosen, than choice of pulleys “TP125“ and “TPC125” is not allowed.

16. Conditions of warning message appearance are corrected (appears when finishing the roller shutter calculation) – “The position place of the oeprating mechanism was wrongly specified. The roller shutter can not be operated. Change the operating mechanism placement and repeat  the calculation”.

17. The algorithm of shutter box choice has been slightly changed for suspension types “Security lock” and “Reinforced security lock”. It means that algorithm of slats quantity calculation for these types of suspensions has also been changed.

18. Curtain winding parameters have been corrected for profiles “AR/55“, “AR/55N“, “ARH/55“ and “ARH/55N“.

19. Curtain winding parameters have been corrected for profiles “PD/45” and “PD/45N”.

20. Wind load parameters and values of maximum surface size have been corrected for profile “AER44m/S”.

21. Values of maximum surface size have been corrected for profile “AG/77”.

22. Wind load standard “SNiP 2.01.07“ has been renamed for “SP 20.13330.2011“.

23. The following reports have been corrected:

- “Commercial offer (standard pricing system)“: advertising text on the top part of the report (abbreviation “SNiP 2.01.07” is changed for abbreviation “SP 20.13330.2011”).

- “Commercial offer (grid pricing system)“: advertising text on the top part of the report (abbreviation “SNiP 2.01.07” is changed for abbreviation “SP 20.13330.2011”).

If you edited models of these reports before then you need to take these changes into consideration because the models of reports are not updated with the program update.

24. Mistakes have been corrected.